## Slide 1: A core Course on Modeling
Introduction to Modeling
0LAB0 0LBB0 0LCB0 0LDB0
c.w.a.m.v.overveld@tue.nl
v.a.j.borghuis@tue.nl
P.12

## Slide 2
Applying SPEA to the lantern problem
Step 1: translate formulas to an ACCEL implementation
Remember:
maxInt = max r  roadc*B(r)
= max r  roadc*(n p h/|Ln-r|3)

## Slide 3
Applying SPEA to the lantern problem
Step 1: translate fromulas to an ACCEL implementation
Remember:
maxInt = max r  roadc*B(r)
= max r  roadc*(n p h/|Ln-r|3)
Earlier we worked with a simpler formula: p/|Ln-r|2.
The extra factor h/|Ln-r| accounts for the effect that the brightness due to lightrays, entering under an angle , is reduced with a factor cos . Notice that cos  = h/|Ln-r|.

## Slide 4
Applying SPEA to the lantern problem
Step 1: translate fromulas to an ACCEL implementation
Remember:
maxInt = max r  roadc*B(r)
= max r  roadc*(n p h/|Ln-r|3)
minInt = min r  roadc*B(r)
= min r  roadc*(n p h/|Ln-r|3)

## Slide 5
Applying SPEA to the lantern problem
Step 1: translate formulas to an ACCEL implementation
maxInt is written as
max r  road B(r),
where B( ... ) is a function returning the total intensity in point r = (l,w). (Height of r is 0, so we ignore the 3rd coordinate.)

## Slide 6
Applying SPEA to the lantern problem
Step 1: translate formulas to an ACCEL implementation
maxInt is written as
max r  road B(r) = max (l,w)  road B(l,w),
We use quantified expressions:
max r  domain B(r)  in ACCEL: #(r, domain, B(r), max)
Remember from Chapter 2?

## Slide 7
Applying SPEA to the lantern problem
Step 1: translate formulas to an ACCEL implementation
maxInt is written as
max r  road B(r) = max (l,w)  road B(l,w),
We use quantified expressions:
max r  domain B(r)  in ACCEL: #(r, domain, B(r), max)

## Slide 8
Applying SPEA to the lantern problem
Step 1: translate formulas to an ACCEL implementation
maxInt is written as
max r  road B(r) = max (l,w)  road B(l,w),
We use quantified expressions:
max r  domain B(r)  in ACCEL: #(r, domain, B(r), max)
A dummy quantity is the first argument of the ACCEL #( ... , ... , ... , ...) function

## Slide 9
Applying SPEA to the lantern problem
Step 1: translate formulas to an ACCEL implementation
maxInt is written as
max r  road B(r) = max (l,w)  road B(l,w),
We use quantified expressions:
max r  domain B(r)  in ACCEL: #(r, domain, B(r), max)
The domain is a set of values, that will be assumed by the dummy. The domain is the second argument in the ACCEL # (..., ..., ..., ...) function.

## Slide 10
Applying SPEA to the lantern problem
Step 1: translate formulas to an ACCEL implementation
maxInt is written as
max r  road B(r) = max (l,w)  road B(l,w),
We use quantified expressions:
max r  domain B(r)  in ACCEL: #(r, domain, B(r), max)
There is a term, probably depending on the dummy (in this case B(r) , depending on r) that is to be evaluated for each value of the dummy taken from the domain. This is the third argument.

## Slide 11
Applying SPEA to the lantern problem
Step 1: translate formulas to an ACCEL implementation
maxInt is written as
max r  road B(r) = max (l,w)  road B(l,w),
We use quantified expressions:
max r  domain B(r)  in ACCEL: #(r, domain, B(r), max)
The instruction ‘max’ tells us what we should do with the outcomes of the term B(r): we should take the maximum. Other quantifications are e.g. the min(imum) or add (summation) and others. This is the fourth argument.

## Slide 12
Applying SPEA to the lantern problem
Step 1: translate formulas to an ACCEL implementation
maxInt is written as
maxr  road B(r) = max(l,w)  road B(l,w),
We use quantified expressions. These can be nested:
max (l,w)  domain B(l,w) =max l  domainL M(l)
where M(l) = max w  domainW B(l,w)

## Slide 13
Applying SPEA to the lantern problem
Step 1: translate formulas to an ACCEL implementation
maxInt is written as
maxr  road B(r) = max(l,w)  road B(l,w),
We use quantified expressions. These can be nested:
max (l,w)  domain B(l,w) =max l  domainL M(l)
so: max (l,w)  domain B(l,w) =
max l  domainL ( max w  domainW B(l,w) )

## Slide 14
Applying SPEA to the lantern problem
Step 1: translate formulas to an ACCEL implementation
maxInt is written as
maxr  road B(r) = max(l,w)  road B(l,w),
We use quantified expressions. These can be nested:
max l  domainL ( max w  domainW B(l,w))  in ACCEL:
#(l, domainL, M(l) , max)

## Slide 15
Applying SPEA to the lantern problem
Step 1: translate formulas to an ACCEL implementation
maxInt is written as
maxr  road B(r) = max(l,w)  road B(l,w),
We use quantified expressions. These can be nested:
max l  domainL ( max w  domainW B(l,w))  in ACCEL:
#(l, domainL, #(w, domainW, B(l,w), max), max)

## Slide 16
Applying SPEA to the lantern problem
Step 1: translate formulas to an ACCEL implementation
maxInt is written
in ACCEL as: #(l,domainL,#(w,domainW,B(l,w),max),max)

## Slide 17
Applying SPEA to the lantern problem
Step 1: translate formulas to an ACCEL implementation
maxInt is written
in ACCEL as: #(l,domainL,#(w,domainW,B(l,w),max),max)
domainL=[0,1,2,...roadLength]=vSeq(0,roadLength+1)

## Slide 18
Applying SPEA to the lantern problem
Step 1: translate formulas to an ACCEL implementation
maxInt is written
in ACCEL as: #(l,domainL,#(w,domainW,B(l,w),max),max)
domainL=[0,1,2,...roadLength]=vSeq(0,roadLength+1)
domainW=[0,1,2,...roadWidth]=vSeq(0,roadWidth+1)

## Slide 19
Applying SPEA to the lantern problem
Step 1: translate formulas to an ACCEL implementation
maxInt is written
in ACCEL as: #(l,domainL,#(w,domainW,B(l,w),max),max)
B(l, w) = n Bn(l, w) – again a quantified expression:
n Bn(l, w)  in ACCEL: B(l,w)=#(n,domainN,Bn(l,w,n),add)

## Slide 20
Applying SPEA to the lantern problem
Step 1: translate formulas to an ACCEL implementation
maxInt is written
in ACCEL as: #(l,domainL,#(w,domainW,B(l,w),max),max)
B(l, w) = n Bn(l, w) – again a quantified expression:
n Bn(l, w)  in ACCEL: B(l,w)=#(n,domainN,Bn(l,w,n),add)
where Bn(l, w, n) = c*p*h /r(l,w,n)3  B(l,w,n)=c*p*h/pow(r(l,w,n),3)

## Slide 21
Applying SPEA to the lantern problem
Step 1: translate formulas to an ACCEL implementation
maxInt is written
in ACCEL as: #(l,domainL,#(w,domainW,B(l,w),max),max)
B(l, w) = n Bn(l, w) – again a quantified expression:
n Bn(l, w)  in ACCEL: B(l,w)=#(n,domainN,Bn(l,w,n),add)
where Bn(l, w, n) = c*p*h /r(l,w,n)3  B(l,w,n)=c*p*h/pow(r(l,w,n),3),
and domainN=[0,1,2, ... nLanterns-1] = vSeq(0,nLanterns)

## Slide 22
Applying SPEA to the lantern problem
Step 1: translate formulas to an ACCEL implementation
maxInt is written
in ACCEL as: #(l,domainL,#(w,domainW,B(l,w),max),max)

## Slide 23
Applying SPEA to the lantern problem
Step 1: translate formulas to an ACCEL implementation
maxInt is written
in ACCEL as: #(l,domainL,#(w,domainW,B(l,w),max),max),
and similar for minInt:
#(l,domainL,#(w,domainW,B(l,w),min),min)

## Slide 24
Applying SPEA to the lantern problem
Step 1: translate formulas to an ACCEL implementation
maxInt is written
in ACCEL as: #(l,domainL,#(w,domainW,B(l,w),max),max)
Finally, we calculate r(l,w,n) using Pythagoras:
r(l,w,n)=sqrt(h*h+(w-Wh)*(w-Wh)+(l-n*dL)*(l-n*dL))

## Slide 25
Applying SPEA to the lantern problem
Step 1: translate formulas to an ACCEL implementation
maxInt is written
in ACCEL as: #(l,domainL,#(w,domainW,B(l,w),max),max)
Finally, we calculate r(l,w,n) using Pythagoras:
r(l,w,n)=sqrt(h*h+(w-Wh)*(w-Wh)+(l-n*dL)*(l-n*dL))
The height of the lanterns, this equals the height difference with r (having height 0).

## Slide 26
Applying SPEA to the lantern problem
Step 1: translate formulas to an ACCEL implementation
maxInt is written
in ACCEL as: #(l,domainL,#(w,domainW,B(l,w),max),max)
Finally, we calculate r(l,w,n) using Pythagoras:
r(l,w,n)=sqrt(h*h+(w-Wh)*(w-Wh)+(l-n*dL)*(l-n*dL))
The distance measured perpendicular to the axis of the road; lanterns are above the road axis.

## Slide 27
Applying SPEA to the lantern problem
Step 1: translate formulas to an ACCEL implementation
maxInt is written
in ACCEL as: #(l,domainL,#(w,domainW,B(l,w),max),max)
Finally, we calculate r(l,w,n) using Pythagoras:
r(l,w,n)=sqrt(h*h+(w-Wh)*(w-Wh)+(l-n*dL)*(l-n*dL))
Distance measured parallel to the axis of the road: lantern nr. n has location n*dL.

## Slide 28
Applying SPEA to the lantern problem
Step 1: translate formulas to an ACCEL implementation
dL=slider(25.5,15,50)
h=slider(5.5,3,30)
p=slider(500.1,100,10000)
intPenalty=paretoMin(paretoHor(-min(minP,minInt)+max(maxP,maxInt)-(maxP-minP)))
totPow=paretoMin(paretoVer(p*nLanterns))
maxP=80
minP=10
roadLength=100
roadWidth=6
Wh=roadWidth/2
maxInt=#(l,vSeq(0,roadLength+1),#(w,vSeq(0,roadWidth+1),B(l,w),max),max)
minInt=#(l,vSeq(0,roadLength+1),#(w,vSeq(0,roadWidth+1),B(l,w),min),min)
B(l,w)=#(n,vSeq(0,nLanterns),Bn(l,w,n),add)
Bn(l,w,n)=c*p*h/pow(r(l,w,n),3)
c=1
r(l,w,n)=sqrt(h*h+(w-Wh)*(w-Wh)+(l-n*dL)*(l-n*dL))
nLanterns=1+roadLength/dL

## Slide 29
Applying SPEA to the lantern problem
Step 1: translate formulas to an ACCEL implementation
dL=slider(25.5,15,50)
h=slider(5.5,3,30)
p=slider(500.1,100,10000)
intPenalty=paretoMin(paretoHor(-min(minP,minInt)+max(maxP,maxInt)-(maxP-minP)))
totPow=paretoMin(paretoVer(p*nLanterns))
maxP=80
minP=10
roadLength=100
roadWidth=6
Wh=roadWidth/2
maxInt=#(l,vSeq(0,roadLength+1),#(w,vSeq(0,roadWidth+1),B(l,w),max),max)
minInt=#(l,vSeq(0,roadLength+1),#(w,vSeq(0,roadWidth+1),B(l,w),min),min)
B(l,w)=#(n,vSeq(0,nLanterns),Bn(l,w,n),add)
Bn(l,w,n)=c*p*h/pow(r(l,w,n),3)
c=1
r(l,w,n)=sqrt(h*h+(w-Wh)*(w-Wh)+(l-n*dL)*(l-n*dL))
nLanterns=1+roadLength/dL
These are the category-I quantities: distance dL, height h, power p

## Slide 30
Applying SPEA to the lantern problem
Step 1: translate formulas to an ACCEL implementation
dL=slider(25.5,15,50)
h=slider(5.5,3,30)
p=slider(500.1,100,10000)
intPenalty=paretoMin(paretoHor(-min(minP,minInt)+max(maxP,maxInt)-(maxP-minP)))
totPow=paretoMin(paretoVer(p*nLanterns))
maxP=80
minP=10
roadLength=100
roadWidth=6
Wh=roadWidth/2
maxInt=#(l,vSeq(0,roadLength+1),#(w,vSeq(0,roadWidth+1),B(l,w),max),max)
minInt=#(l,vSeq(0,roadLength+1),#(w,vSeq(0,roadWidth+1),B(l,w),min),min)
B(l,w)=#(n,vSeq(0,nLanterns),Bn(l,w,n),add)
Bn(l,w,n)=c*p*h/pow(r(l,w,n),3)
c=1
r(l,w,n)=sqrt(h*h+(w-Wh)*(w-Wh)+(l-n*dL)*(l-n*dL))
nLanterns=1+roadLength/dL
These are the category-II quantities: penalties for energy consumption, p*nLanterns,
and a penalty in case maxInt > maxP or
minInt < minP

## Slide 31
Applying SPEA to the lantern problem
Step 1: translate formulas to an ACCEL implementation
dL=slider(25.5,15,50)
h=slider(5.5,3,30)
p=slider(500.1,100,10000)
intPenalty=paretoMin(paretoHor(-min(minP,minInt)+max(maxP,maxInt)-(maxP-minP)))
totPow=paretoMin(paretoVer(p*nLanterns))
maxP=80
minP=10
roadLength=100
roadWidth=6
Wh=roadWidth/2
maxInt=#(l,vSeq(0,roadLength+1),#(w,vSeq(0,roadWidth+1),B(l,w),max),max)
minInt=#(l,vSeq(0,roadLength+1),#(w,vSeq(0,roadWidth+1),B(l,w),min),min)
B(l,w)=#(n,vSeq(0,nLanterns),Bn(l,w,n),add)
Bn(l,w,n)=c*p*h/pow(r(l,w,n),3)
c=1
r(l,w,n)=sqrt(h*h+(w-Wh)*(w-Wh)+(l-n*dL)*(l-n*dL))
nLanterns=1+roadLength/dL
These are the category-III quantities: dimensions of the road, maxP, minP and the factor c

## Slide 32
Applying SPEA to the lantern problem
Step 1: translate formulas to an ACCEL implementation
dL=slider(25.5,15,50)
h=slider(5.5,3,30)
p=slider(500.1,100,10000)
intPenalty=paretoMin(paretoHor(-min(minP,minInt)+max(maxP,maxInt)-(maxP-minP)))
totPow=paretoMin(paretoVer(p*nLanterns))
maxP=80
minP=10
roadLength=100
roadWidth=6
Wh=roadWidth/2
maxInt=#(l,vSeq(0,roadLength+1),#(w,vSeq(0,roadWidth+1),B(l,w),max),max)
minInt=#(l,vSeq(0,roadLength+1),#(w,vSeq(0,roadWidth+1),B(l,w),min),min)
B(l,w)=#(n,vSeq(0,nLanterns),Bn(l,w,n),add)
Bn(l,w,n)=c*p*h/pow(r(l,w,n),3)
c=1
r(l,w,n)=sqrt(h*h+(w-Wh)*(w-Wh)+(l-n*dL)*(l-n*dL))
nLanterns=1+roadLength/dL
These are the category-IV quantities: the max- and min intensities
and the functions needed to calculate these;
the number of lanterns given the length of the road,
and the half width of the road.

## Slide 33
Applying SPEA to the lantern problem
Step 1: translate formulas to an ACCEL implementation
dL=slider(25.5,15,50)
h=slider(5.5,3,30)
p=slider(500.1,100,10000)
intPenalty=paretoMin(paretoHor(-min(minP,minInt)+max(maxP,maxInt)-(maxP-minP)))
totPow=paretoMin(paretoVer(p*nLanterns))
maxP=80
minP=10
roadLength=100
roadWidth=6
Wh=roadWidth/2
maxInt=#(l,vSeq(0,roadLength+1),#(w,vSeq(0,roadWidth+1),B(l,w),max),max)
minInt=#(l,vSeq(0,roadLength+1),#(w,vSeq(0,roadWidth+1),B(l,w),min),min)
B(l,w)=#(n,vSeq(0,nLanterns),Bn(l,w,n),add)
Bn(l,w,n)=c*p*h/pow(r(l,w,n),3)
c=1
r(l,w,n)=sqrt(h*h+(w-Wh)*(w-Wh)+(l-n*dL)*(l-n*dL))
nLanterns=1+roadLength/dL

## Slide 34
Applying SPEA to the lantern problem
Step 1: translate formulas to an ACCEL implementation
The actual script has few additional features to plot
B(r).
maxP: no blinding
minP: enough contrast
intensity on road axis
intensity on road border

## Slide 35
Applying SPEA to the lantern problem
Step 1: translate formulas to an ACCEL implementation
The actual script has few additional features to plot
B(r).

## Slide 36
Applying SPEA to the lantern problem
Step 1: translate formulas to an ACCEL implementation
The actual script has few additional features to plot
B(r).
It does produce a Pareto plot.
But it is very slow: no actual optimization possible.
intPenalty
totPow

## Slide 37
Applying SPEA to the lantern problem
Step 2: make the script more efficient  optimization
Reasons for slow performance:
iterate over l
iterate over w
iterate over n
assume maxInt occurs underneath a lantern
assume minInt occurs on the border, in the middle between two lanterns
take not too many lanterns into account

## Slide 38
Applying SPEA to the lantern problem
Step 2: make the script more efficient  optimization
dL=slider(25.5,15,50)
h=slider(5.5,3,30)
p=slider(500.1,100,10000)
intPenalty=paretoMin(paretoHor(-min(minP,minInt)+max(maxP,maxInt)-(maxP-minP)))
totPow=paretoMin(paretoVer(p*nLanterns))
maxP=80
minP=10
roadLength=100
roadWidth=6
Wh=roadWidth/2
maxInt=#(l,vSeq(0,roadLength+1),#(w,vSeq(0,roadWidth+1),B(l,w),max),max)
minInt=#(l,vSeq(0,roadLength+1),#(w,vSeq(0,roadWidth+1),B(l,w),min),min)
B(l,w)=#(n,vSeq(0,nLanterns),Bn(l,w,n),add)
Bn(l,w,n)=c*p*h/pow(r(l,w,n),3)
c=1
r(l,w,n)=sqrt(h*h+(w-Wh)*(w-Wh)+(l-n*dL)*(l-n*dL))
nLanterns=1+roadLength/dL

## Slide 39
Applying SPEA to the lantern problem
Step 2: make the script more efficient  optimization
dL=slider(25.5,15,50)
h=slider(5.5,3,30)
p=slider(500.1,100,10000)
intPenalty=paretoMin(paretoHor(-min(minP,minInt)+max(maxP,maxInt)-(maxP-minP)))
totPow=paretoMin(paretoVer(p*nLanterns))
maxP=80
minP=10
roadLength=100
roadWidth=6
Wh=roadWidth/2
maxInt=#(l,vSeq(0,roadLength+1),#(w,vSeq(0,roadWidth+1),B(l,w),max),max)
minInt=#(l,vSeq(0,roadLength+1),#(w,vSeq(0,roadWidth+1),B(l,w),min),min)
B(l,w)=#(n,vSeq(0,nLanterns),Bn(l,w,n),add)
Bn(l,w,n)=c*p*h/pow(r(l,w,n),3)
c=1
r(l,w,n)=sqrt(h*h+(w-Wh)*(w-Wh)+(l-n*dL)*(l-n*dL))
nLanterns=1+roadLength/dL

## Slide 40
Applying SPEA to the lantern problem
Step 2: make the script more efficient  optimization
dL=slider(25.5,15,50)
h=slider(5.5,3,30)
p=slider(500.1,100,10000)
intPenalty=paretoMin(paretoHor(-min(minP,minInt)+max(maxP,maxInt)-(maxP-minP)))
totPow=paretoMin(paretoVer(p*nLanterns))
maxP=80
minP=10
roadLength=100
roadWidth=6
Wh=roadWidth/2
maxInt=B(dL*round(nLanterns/2),Wh)
minInt=B(dL*(round(nLanterns/2)+round(nLanterns/2)+1)/2,0)
B(l,w)=#(n,vSeq(round(nLanterns/2)-N,round(nLanterns/2)+N+1),Bn(l,w,n),add)
Bn(l,w,n)=c*p*h/pow(r(l,w,n),3)
c=1
r(l,w,n)=sqrt(h*h+(w-Wh)*(w-Wh)+(l-n*dL)*(l-n*dL))
nLanterns=1+roadLength/dL
assumption: highest intensity right underneath middle lantern
assumption: lowest intensity in the middle between two mid lanterns on the border of the road
assumption: sufficiently accurate estimate of B taking 2N lanterns into account. Tricky: how large is N? (could depend on h and dL!)
Approach: for reasonable dL and h, experiment with N to see if convergence occurs

## Slide 41
Applying SPEA to the lantern problem
Step 2: make the script more efficient  optimization
Model is fast enough to enable Pareto genetic optimization.
But the difference between acceptable (intPenalty==0) and non-acceptable (intPenalty>0) is difficult to see: intPenalty should be defined better.
intPenalty
totPow

## Slide 42
Applying SPEA to the lantern problem
Step 2: make the script more efficient  optimization
Model is fast enough to enable Pareto genetic optimization.
But the difference between acceptable (intPenalty==0) and non-acceptable (intPenalty>0) is difficult to see: intPenalty should be defined better.
Now:
-min(minP,minInt)+max(maxP,maxInt)-(maxP-minP)
Better:
log(0.00001-min(minP,minInt)+max(maxP,maxInt)-(maxP-minP))
compare penalty q1=x
with penalty q2=log(0.00001+x):
for x=0, q2= -5
for x>0, q2= much bigger

## Slide 43
Applying SPEA to the lantern problem
Step 2: make the script more efficient  optimization
Now:
-min(minP,minInt)+max(maxP,maxInt)-(maxP-minP)
Better:
log(0.00001-min(minP,minInt)+max(maxP,maxInt)-(maxP-minP))
dL=slider(25.5,15,50)
h=slider(5.5,3,30)
p=slider(500.1,100,10000)
intPenalty=paretoMin(paretoHor(-min(minP,minInt)+max(maxP,maxInt)-(maxP-minP)))
totPow=paretoMin(paretoVer(p*nLanterns))
maxP=80
minP=10
roadLength=100
roadWidth=6
Wh=roadWidth/2
maxInt=B(dL*round(nLanterns/2),Wh)
minInt=B(dL*(round(nLanterns/2)+round(nLanterns/2)+1)/2,0)
B(l,w)=#(n,vSeq(round(nLanterns/2)-N,round(nLanterns/2)+N+1),Bn(l,w,n),add)
Bn(l,w,n)=c*p*h/pow(r(l,w,n),3)
c=1
r(l,w,n)=sqrt(h*h+(w-Wh)*(w-Wh)+(l-n*dL)*(l-n*dL))
nLanterns=1+roadLength/dL

## Slide 44
Applying SPEA to the lantern problem
Step 3: better penalty function
Now:
-min(minP,minInt)+max(maxP,maxInt)-(maxP-minP)
Better:
log(0.00001-min(minP,minInt)+max(maxP,maxInt)-(maxP-minP))
dL=slider(25.5,15,50)
h=slider(5.5,3,30)
p=slider(500.1,100,10000)
intPenalty=paretoMin(paretoHor(-min(minP,minInt)+max(maxP,maxInt)-(maxP-minP)))
totPow=paretoMin(paretoVer(p*nLanterns))
maxP=80
minP=10
roadLength=100
roadWidth=6
Wh=roadWidth/2
maxInt=B(dL*round(nLanterns/2),Wh)
minInt=B(dL*(round(nLanterns/2)+round(nLanterns/2)+1)/2,0)
B(l,w)=#(n,vSeq(round(nLanterns/2)-N,round(nLanterns/2)+N+1),Bn(l,w,n),add)
Bn(l,w,n)=c*p*h/pow(r(l,w,n),3)
c=1
r(l,w,n)=sqrt(h*h+(w-Wh)*(w-Wh)+(l-n*dL)*(l-n*dL))
nLanterns=1+roadLength/dL

## Slide 45
Applying SPEA to the lantern problem
Step 3: better penalty function
Now:
-min(minP,minInt)+max(maxP,maxInt)-(maxP-minP)
Better:
log(0.00001-min(minP,minInt)+max(maxP,maxInt)-(maxP-minP))
dL=slider(25.5,15,50)
h=slider(5.5,3,30)
p=slider(500.1,100,10000)
intPenalty=paretoMin(paretoHor(log(0.00001-min(minP,minInt)+max(maxP,maxInt)-(maxP-minP))))
totPow=paretoMin(paretoVer(p*nLanterns))
maxP=80
minP=10
roadLength=100
roadWidth=6
Wh=roadWidth/2
maxInt=B(dL*round(nLanterns/2),Wh)
minInt=B(dL*(round(nLanterns/2)+round(nLanterns/2)+1)/2,0)
B(l,w)=#(n,vSeq(round(nLanterns/2)-N,round(nLanterns/2)+N+1),Bn(l,w,n),add)
Bn(l,w,n)=c*p*h/pow(r(l,w,n),3)
c=1
r(l,w,n)=sqrt(h*h+(w-Wh)*(w-Wh)+(l-n*dL)*(l-n*dL))
nLanterns=1+roadLength/dL

## Slide 46
Applying SPEA to the lantern problem
Step 3: better penalty function
New penalty function separates solutions with maxIntmaxP and minIntminP from those that don’t satisfy this condition.
(remember the difference between requirements and wishes: energy low wish; visibility constraints  requirement)
intPenalty
totPow
intPenalty == -5
intPenalty >> -5

## Slide 47
Applying SPEA to the lantern problem
Step 3: better penalty function
Problem now is that the found optima seem to lie close to the extremes of the category-I intervals.
Save this problem for interpretation phase.

## Slide 48
Summary
Application of SPEA
Translate conceptual model into formal (mathematical) model
Translate mathematical model to script: may require quantised expressions, user defined functions, additional scaffolding quantities (e.g., plotting)
Performance issues: re-think assumptions
Presentation issues: re-think penalties
Interpretation issues: are cat.-I ranges adequate?